sed
A language for processing text streams

---
Introduction
- It is a programming language
- sed is an abbreviation for stream editor
- It is a part of POSIX
- sed precedes awk

---
Execution model
- Input stream is a set of lines
- Each line is a sequence of characters
- Two data buffers are maintained: active pattern space and auxiliary hold space
- For each line of input, an execution cycle is performed loading the line into the pattern space
- During each cycle, all the statements in the script are executed in the sequence for matching address pattern for actions specified with the options provided

---
usage
- Single line at the command line
  sed -e ‘s/hello/world/g‘ input.txt
- Script interpreted by sed
  sed -f ./myscript.sed input.txt
myscript.sed
#!/usr/bin/sed -f
2,8s/hello/world/g

---
sed statements
address pattern
;
:label
action
options
address
Single Character action
Same as “ed” or “ex”
address , range
!
negation
Depends on the action

---
Grouping commands
{ cmd; cmd; }

---
address
5
$
Selecting by numbers
%
1~3
/regexp/
Selecting by text matching
/regexp1/,/regexp2/
range addresses
/regexp/, +4
5,15
/regexp/, ~2
5,/regexp/

---
actions
p	Print the pattern space
d	Delete the pattern space
s	Substitute using regex match s/pattern/replacement/g
=	Print current input line number, \n
#	comment
i	Insert above current line
a	Append below current line
c	Change current line

---
programming
b label	Branch unconditionally to label
:label	Specify location of label for branch command
N	Add a new line to the pattern space and append next line of input into it.
q	Exit sed without processing any more commands or input lines
t label	Branch to label only if there was a successful substitution was made
T label	Branch to label only if there was no successful substitution was made
w filename	Write pattern space to filename
x	Exchange the contents of hold and pattern spaces

---
bash + sed
- Including sed inside shell script
- heredoc feature
- Use with other shell scripts on command line using pipe

---
sed is available everywhere !
sed is a meant for text processing, fast in execution
use sed to pre-process input for further processing